## Slide 1: CAOS Project - HacOSsim
Fabio Lorenzato (332186) - Alessandro Milani (s332136) - Matteo Scrusatone (332153)

## Slide 2: Real-Time Operating System
The extensive documentation available
A really active forum
That one being open source, of course
Prior knowledge of it could be useful in the future, because it’s backed by Amazon

## Slide 3: Board & Emulator
We emulated the Luminary Micro Stellaris LM3S6965EVB thanks to Qemu.
This board has some interesting feature like:
256k Flash memory and 64k SRAM
Lots of featured and interfaces available (Timers, UARTs, ADC, I2C, SSI interfaces, . . . )
Some graphical drivers already available
lots of guided examples

## Slide 4: Display Demo
Functionalities implemented:
HW
  Display
      SW
        Semaphore
        message queue

## Slide 5: Input Demo
Functionalities implemented:
HW
  UART device
SW
  Keyboard input function

## Slide 6: CHAOS demo
Other implementation:
SW
  More task that have access to the display simultaneously
  Bitmap
  Pseudo Random Generator

## Slide 7: Pong
Funny to play until you comprehend that you cannot win.

## Slide 8: EDF implementation
New scheduler has to be enabled.
New ready list to handle tasks, made possible by adding the period to the Task PCB.

## Slide 9: EDF implementation
New way to create tasks(period instead of priority).
Idle task became periodic, which will never run unless it’s necessary.

## Slide 10: EDF implementation
Changed the logic for context switch.

## Slide 11: EDF Performance Evaluation
 | Task period | Execution time
Task 1 | 40 | 11
Task 2 | 8 | 3
Task 3 | 6 | 2

## Slide 12: EDF benchmark
Effectiveness:
42.358% reduction of switch in
56.311% reduction of idle ticks
More balanced overall lateness
 | Default | EDF
Idle ticks | 103 | 58
Switch in | 1289 | 546
Lateness Task 1 | -13.93 | -6.31
Lateness Task 2 | -1.47 | -4.32
Lateness Task 3 | -1.57 | -4.0
*All results in ticks

## Slide 13: Project contribution
Task | Lorenzato | Milani | Scursatone
Repo setup and configuration | X | X | X
Demo code implementation | X | X | X
Scheduling algorithm implementation | X |  | 
Performance evaluation | X | X | 
Report and Documentation | X | X | X

## Slide 14: Thanks for your attention!